Design and Application of Gain Division Multiple Access

Gain division multiple access (GDMA) is a non-orthononal multiple access methods, which can simultaneously transmit multiple users in the same resource. In the thesis, we use clustering as a pilot-free channel estimation technique to obtain channel state information (CSI). Space Time Block Code (STBC) is a technique used in wireless communications, which can get more diversity by using multiple antennas and multiple time slots. We use STBC to make our system more robust.

We also combine GDMA with orthogonal frequency division multiplexing (OFDM) in the polar-coded scheme. With the characteristic of polar code, we can solve the phase ambiguity of pilot-free channel estimation and reduce the peak-to-average power ratio (PAPR) at the same time.

Low density signature code division multiple access (LDS-CDMA) and Sparse code multiple access (SCMA) are non-orthogonal multiple access methods, where SCMA is a method derived from LDS-CDMA with a special design of signal constellation. In the literature, we compare GDMA, LDS-CDMA, and SCMA under Rayleigh fading channels in many different schemes.

low densitysignature code division multiple access (LDS-CDMA) and Sparsecode multiple access (SCMA) are non-orthogonal multiple accessmethods, where SCMA is a method derived from LDS-CDMAwith a special design of signal constellation. In this paper, we com-pare their performances for transmission over Rayleigh fadingchannels. Simulation results show that the special constellationdesign of SCMA does not provide any gain in Rayleigh fadingchannels. We see that LDS-CDMA scheme based on 4 resourcesoutperforms the GDMA based on a single resource under perfectchannel state information (CSI). By using more resources anderror-correcting codes, GDMA can provide error rates similarto LDS-CDMA

 Moreover....OFDM.....bla....PAPR.....clustering.....RACH

======NBC paper

About complexity

1. Clustering : not many users. comparing to polar decoder, the complexity of clustering is nothing

2. polar encoder ( PAPR) pre-calculated FFT result and bit flipping for each subcarrier

3. polar decoder : LDPC vs polar