## Slide 1: Code Assisted Iterative Channel Estimation for OFDM Systems over Multipath Fast-Fading Channel
Speaker : Yi-Ru Chen
Advisor : Prof. Mao-Chao Lin, Prof. Huang-Chang Lee
June 06, 2020

## Slide 2: Motivation
Orthogonal frequency-division multiplexing (OFDM)
  High data rate transmission with multiple orthogonal subcarriers
  Robustness against frequency-selective fading channels
Over multipath fast-fading channels
  Doppler spread caused by Doppler effect results in inter-carrier interference (ICI)
  Channel is time-varying if the OFDM symbol duration exceeding coherence time
  Using grouped preambles to observe the ICI for channel estimation but lower spectrum efficiency
Code Assisted Iterative Channel Estimation
  Adopt decoding information to assist the channel estimation
  Reduce the number of the preambles for higher spectrum efficiency
  Observe the ICI with the single preamble set

## Slide 3: Outline
Multipath Fast-Fading Channel
  Channel Characteristics
  Simulated Channel Model
Coded OFDM System
  System Model and Derivation
  Polynomial-Basis Expansion Model
  Frequency-Domain Equalization Techniques for ICI Mitigation
Preamble and Codeword Arrangement
Code Assisted Iterative Channel Estimation
  Least Square Based Model
  Kalman filter Based Model

## Slide 4: Outline
Multipath Fast-Fading Channel
  Channel Characteristics
  Simulated Channel Model
Coded OFDM System
  System Model and Derivation
  Polynomial-Basis Expansion Model
  Frequency-Domain Equalization Techniques for ICI Mitigation
Preamble and Codeword Arrangement
Code Assisted Iterative Channel Estimation
  Least Square Based Model
  Kalman filter Based Model

## Slide 5: Channel Characteristics
Channel gain varies as frequency and time, caused by Multipath propagation and Doppler effect
Frequency selectivity and Doppler spread lead to inter-symbol interference(ISI) and inter-carrier interference(ICI) respectively
ISI and ICI result in the performance loss and error floor
  ISI can be eliminated by exploiting the cyclic prefix (CP)
  OFDM systems are more sensitive to the time-varying channel
  In high Doppler spread environment, how to efficiently reduce ICI effect is critical for the receiver design

## Slide 6: Simulated Channel Model
    Time-varying L-taps channel impulse response(CIR)
  Frequency selectivity
    Six-taps exponentially-decaying CIR [1] with decay rate dB
    Power delay profile
  Time variant
        Jakes’ model associated with Rayleigh distribution [2] with normalized Doppler frequency
        Autocorrelation function
[1] D.R. Morgan, “Analysis and Realization of an Exponentially-Decaying Impulse Response Model for Frequency-Selective Fading Channels,” IEEE Signal Process. Lett., vol.15, pp.441-444, 2008
[2] Zheng, Y., Xiao, C.: ‘Improved models for the generation of multiple uncorrelated Rayleigh fading waveforms’, IEEE Commun. Lett., 2002
: sample time interval

## Slide 7: Outline
Multipath Fast-Fading Channel
  Channel Characteristics
  Simulated Channel Model
Coded OFDM System
  System Model and Derivation
  Polynomial-Basis Expansion Model
  Frequency-Domain Equalization Techniques for ICI Mitigation
Preamble and Codeword Arrangement
Code Assisted Iterative Channel Estimation
  Least Square Based Model
  Kalman filter Based Model

## Slide 8: System Model and Derivation

## Slide 9: System Model and Derivation
The L-taps CIR when transmitting k-th data of m-th OFDM symbol can be expressed as where
The k-th time-domain received signal of the m-th OFDM symbol is given by and where is complex Gaussian noise and is the convolution matrix defined as with

## Slide 10: System Model and Derivation
The corresponding frequency-domain received signal can be calculated as where is normalized FFT matrix and is the channel matrix given by
The k-th frequency-domain received signal of the m-th OFDM symbol can be decomposed into three parts as follows: where is inter-carrier interference term
Observe ICI to estimate the time-varying CIR, then the channel matrix can derived from the estimated CIR

## Slide 11: Polynomial-Basis Expansion Model (P-BEM)
For the -th tap, the channel gains corresponding to the other sample time of m-th OFDM symbol can be approximated as Q-order polynomial [3] and where is the basis matrix and is BEM coefficient vector of the -th tap of m-th OFDM symbol
The BEM coefficient vector of m-th OFDM symbol can be expressed as
[3] Z. Tang, R. C. Cannizzaro, G. Leus, and P. Banelli, “Pilot-assisted time-varying channel estimation for OFDM systems,” IEEE Trans. Signal Process., vol. 55, no. 5, pp. 2226–2238, May 2007.

## Slide 12: Frequency-Domain Equalization Techniques for ICI Mitigation
  Assume that the channel matrix is perfectly estimated
  MMSE equalizer [4]
    To minimize the cost function according to orthogonality principle
    The detected signal can be calculated by where is the variance of channel noise
    It has high complexity due to matrix inversion
[4] Kwanghoon Kim, Hyuncheol Park, “A Low Complexity ICI Cancellation Method for High Mobility OFDM Systems”

## Slide 13: Frequency-Domain Equalization Techniques for ICI Mitigation
  ICI power distribution show that if the subcarrier distance d is greater than a certain value then the power is almost negligible

## Slide 14: Frequency-Domain Equalization Techniques for ICI Mitigation
  Only keep the elements of the channel matrix satisfied that

## Slide 15: Frequency-Domain Equalization Techniques for ICI Mitigation
  Only keep the elements of the channel matrix satisfied that
    Partial Equalization [4] Replace with a partial channel matrix
      Input:
      Output: where is k-th column of
[4] Kwanghoon Kim, Hyuncheol Park, “A Low Complexity ICI Cancellation Method for High Mobility OFDM Systems”

## Slide 16: Frequency-Domain Equalization Techniques for ICI Mitigation
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading; ,
FFT size | 1024
Modulation | 16-QAM
Channel model | 
Uncoded OFDM

## Slide 17: Outline
Multipath Fast-Fading Channel
  Channel Characteristics
  Simulated Channel Model
Coded OFDM System
  System Model and Derivation
  Polynomial-Basis Expansion Model
  Frequency-Domain Equalization Techniques for ICI Mitigation
Preamble and Codeword Arrangement
Code Assisted Iterative Channel Estimation
  Least Square Based Model
  Kalman filter Based Model

## Slide 18: Preamble Arrangement
f

## Slide 19: Preamble Arrangement
  L groups consisting of equally-powered pilot tones in every OFDM symbol, and the positions of pilot tons can be represented as
    The number of groups depends on the number of channel taps
    The total of the pilot tones should be greater or equal to (Q+1), where Q is the polynomial order of P-BEM
    Groups should be equally spaced, which is optimal set
f
The proof is shown in p.22
Note

## Slide 20: Preamble Arrangement
  Ex. N = 16 and L = 3
  In this work, we prefer the lower and adopts error-correcting code to assist channel estimation for better spectrum efficiency
  Focus on how to arrange the codewords and adjust block lengths so as to get the enough correct information for channel estimation

## Slide 21: Preamble Arrangement
  Conventional pilot-aided least square based channel estimation Based on P-BEM, the frequency-domain received signal can be represented as
    : Approximate error
  is also called as measurement equation

## Slide 22: Preamble Arrangement
  Conventional pilot-aided least square based channel estimation
    Select the rows of corresponding to the positions of pilot tones and ignore the approximate error, then
    Find the least square (LS) solution of If the value is less than , we have an under-determined system and a non-unique solution

## Slide 23: Codeword Arrangement
    Since channel is frequency-selective, Arranging multiple sub-codewords can lower the probability of the event that all sub-codeword are incorrect
    Criterion
      where is the syndrome of the sub-codeword with

## Slide 24: Codeword Arrangement
    Two (2048, 1024) LDPC codewords
Use -LDPC code to generate two codewords
(16-QAM)
Codeword 1
Codeword 2
Pilot group bits (4* bits)

## Slide 25: Codeword Arrangement
    Two (2048, 1024) LDPC codewords
Use -LDPC code to generate two codewords
(16-QAM)
Codeword 1
Codeword 2
Pilot group bits (4* bits)

## Slide 26: Codeword Arrangement
    Four (1024, 512) LDPC codewords
Use -LDPC code to generate two codewords
(16-QAM)
Pilot group bits (4* bits)
Codeword 4
Codeword 1
Codeword 2
Codeword 3

## Slide 27: Codeword Arrangement
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading; ,
FEQ | PMMSE, D = 10
Code Rate | 0.5
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Coded OFDM

## Slide 28: Codeword Arrangement
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading; ,
FEQ | PMMSE, D = 10
Code Rate | 0.5
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Coded OFDM

## Slide 29: Preamble Arrangement
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading; ,
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Polynomial Order | 
Coded OFDM

## Slide 30: Preamble Arrangement
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading; ,
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Polynomial Order | 
Coded OFDM

## Slide 31: Preamble Arrangement
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading; ,
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Polynomial Order | 
Coded OFDM

## Slide 32: Outline
Multipath Fast-Fading Channel
  Channel Characteristics
  Simulated Channel Model
Coded OFDM System
  System Model and Derivation
  Polynomial-Basis Expansion Model
  Frequency-Domain Equalization Techniques for ICI Mitigation
Preamble and Codeword Arrangement
Code Assisted Iterative Channel Estimation
  Least Square Based Model
  Kalman filter Based Model

## Slide 33: Code Assisted Iterative Channel Estimation
The measurement equation
  Estimated measurement matrix
  : Augmented noise including the channel noise, approximation error and detection error
Two cases is considered according to the decoding results
  Case 1:
  Case 2:

## Slide 34: Code Assisted Iterative Channel Estimation
Get the enough information with minimized detection error from decoding results
  Case1: Corrected sub-codewords with the corresponding positions
    Detected data symbol
    The measurement equation can be represented as where with and

## Slide 35: Code Assisted Iterative Channel Estimation
Get the enough information with minimized detection error from decoding results
  Case 2: LLR-based detection
    Soft-detected data symbol
    Variance of detection error
    The measurement equation can be represented as where with and

## Slide 36: Least Square Based Model
Partial MMSE
Equalizer
Pilot-Aided LS-based Channel Estimation (p.22)
Multiple LDPC
Sub-Blocks Decoding
Code-Assisted
LS-based Iterative
Channel Estimation
End
: OFDM symbol index
Remodulation

## Slide 37: Least Square Based Model
The channel statistical property is unnecessary
The estimated BEM coefficients from least square solution is given by

## Slide 38: Least Square Based Model
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading, .1
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 8 groups, = 1
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 
Polynomial Order | 
Coded OFDM

## Slide 39: Least Square Based Model
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading, .1
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 8 groups, = 1
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 
Polynomial Order | 
Coded OFDM

## Slide 40: Least Square Based Model
Improvement of LLR-based detection
  Since some detection errors are included when using LLR-based detection
  Store the previous information including the signal and for improving the accuracy for current symbol
The extended measurement equation will be
    The corresponding LS solution is given by

## Slide 41: Least Square Based Model
Partial MMSE
Equalizer
Pilot-Aided LS-based Channel Estimation
Multiple LDPC
Sub-Blocks Decoding
Code-Assisted
LS-based Iterative
Channel Estimation
End
: OFDM symbol index
Remodulation
Store Data

## Slide 42: Least Square Based Model
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading, .1
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 8 groups, = 1
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 
Polynomial Order | 
Coded OFDM

## Slide 43: Least Square Based Model
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading, .1
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 8 groups, = 1
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 
Polynomial Order | 
Coded OFDM

## Slide 44: Least Square Based Model
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading, .1
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 8 groups, = 3
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 
Polynomial Order | 
Coded OFDM

## Slide 45: Least Square Based Model
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading, .1
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 8 groups, = 3
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 
Polynomial Order | 
Coded OFDM

## Slide 46: Kalman Filter-Based Model
    Autoregressive model (AR) for BEM coefficients The time variation of the BEM coefficients can be approached by the one-order AR process
      : Transition matrix
      : Process noise with covariance matrix
    Assuming that the channel statistical properties is known
      The tap power delay profile with decay factor 𝛼
      The l-th tap time-correlation matrix of and
      The time-correlation matrix of BEM coefficients for the l-th tap

## Slide 47: Kalman Filter-Based Model
    Autoregressive model (AR) for BEM coefficients The time variation of the BEM coefficients can be approached by the one-order AR process
      : Transition matrix
      : Process noise with covariance matrix
    Assuming that the channel statistical properties is known

## Slide 48: Kalman Filter-Based Model
  Iterative Kalman-based AR model
  Correlation matrix of augment noise( and )
    : Partial augmented noise with correlation matrix
    : Augmented noise with correlation matrix where
Process Equation:
Measurement Equation:
for
for

## Slide 49: Kalman Filter-Based Model
    Denotations
      Estimated BEM coefficients given and
      Predicted BEM coefficients given and
      Correlation matrix of the coefficient-error given and
      Predicted correlation matrix of the coefficient-error given and
      Kalman Gain
    Initialization
      Time update
        and
      Measurement update Select the rows of corresponding to the positions of the pilot tones P
Measurement Equation:

## Slide 50: Kalman Filter-Based Model

## Slide 51: Kalman Filter-Based Model

## Slide 52: Kalman Filter-Based Model

## Slide 53: Kalman Filter-Based Model

## Slide 54: Kalman Filter-Based Model

## Slide 55: Kalman Filter-Based Model

## Slide 56: Kalman Filter-Based Model

## Slide 57: Kalman Filter-Based Model
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading, .1
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 8 groups, = 3
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 
Polynomial Order | 
Coded OFDM

## Slide 58: Kalman Filter-Based Model
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading, .1
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 8 groups, = 3
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 
Polynomial Order | 
Coded OFDM

## Slide 59: Kalman Filter-Based Model
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading, .1
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 8 groups, = 3
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 
Polynomial Order | 
Coded OFDM

## Slide 60: Kalman Filter-Based Model
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading, .1
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 8 groups, = 3
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Codeword Arrangement | 4*(1024, 512)
Pilot Arrangement | 
Polynomial Order | 
Coded OFDM

## Slide 61: Kalman Filter-Based Model
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading, .1
FEQ | PMMSE, D = 10
Code Rate | 0.5
Pilot Arrangement | 8 groups, = 3
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Pilot Arrangement | 
Polynomial Order | 
Coded OFDM

## Slide 62: Kalman Filter-Based Model
FFT size | 1024
Modulation | 16-QAM
Channel model | Fast-fading, .1
FEQ | PMMSE, D = 10
Code Rate | 0.5
Pilot Arrangement | 8 groups, = 3
Polynomial Order | 
FFT size | 1024
Modulation | 16-QAM
Channel model | 
FEQ | PMMSE, D = 10
Code Rate | 0.5
Pilot Arrangement | 
Polynomial Order | 
Coded OFDM

## Slide 63: References
D.R. Morgan, “Analysis and Realization of an Exponentially-Decaying Impulse Response Model for Frequency-Selective Fading Channels,” IEEE Signal Process. Lett., vol.15, pp.441-444, 2008
Y. P. Lin, S. M. Phoong, and P. P. Vaidyanathan, Filter Zheng, Y., Xiao, C.: ‘Improved models for the generation of multiple uncorrelated Rayleigh fading waveforms’, IEEE Commun. Lett., 2002
Z. Tang, R. C. Cannizzaro, G. Leus, and P. Banelli, “Pilot-assisted time-varying channel estimation for OFDM systems,” IEEE Trans. Signal Process., vol. 55, no. 5, pp. 2226–2238, May 2007.
Kwanghoon Kim, Hyuncheol Park, “A Low Complexity ICI Cancellation Method for High Mobility OFDM Systems”
Huang-Chang Lee, Alex Gong, “A Compressed Sensing Estimation Technique for Doubly Selective Channel in OFDM Systems”
H. Nguyen-Le, T. Le-Ngoc and N. H. Tran, "Iterative Receiver Design With Joint Doubly Selective Channel and CFO Estimation for Coded MIMO-OFDM Transmissions," Oct. 2011.
Stefania, Sesia Issam, Toufik, Matthew Baker, “LTE – The UMTS Long Term Evolution: From Theory to Practice, Second Edition”
B. Lu, G. Yue, and X. Wang, ‘‘Performance analysis and design optimization of LDPC-coded MIMO OFDM systems,’’ IEEE Trans. Signal Process., vol. 52, no. 2, pp. 348–361, Feb. 2004
[1]
[2]
[3]
[4]
[5]
[6]
[7]
[8]

## Slide 64: Convolution Matrix
Superscript: sample time index
Subscript: delay tap index
,